| Meeting Date | 29 May 2018 | Meeting Time | 10.00-11.00 ET / 15.00-16.00 GMT |
| --- | --- | --- | --- |
| Project | Testing & Interoperability, In-Home Wi-Fi Guidelines, Roaming Work Group |
| Project chaired by | Michael Sym (BSG Wireless), John Bahr (CableLabs), Erinn Hall (AT&T) |
| To | tbd |
| Subject | MAC randomization impacts |
| Action ID Prefix | N/A |

Dear Sirs,

Currently, iOS, Android, and Windows  anonymize the MAC address during probe requests whilestill uses the true MAC address when connecting to the network. Further addressing the need of user privacy, in Android P new development (ref), Android plans to create a unique, anonymous MAC for each SSID that the device connects to:

“Connected mode randomization is a developer feature only and would be default off for Android P. Our main goal this year is to get a soak time in the industry and get feedback from partners such as yourself who depend on mac address identifier. It gives time for the ecosystem to adapt to new behavior once we roll out in subsequent releases as default behavior.

In O, we released Probe mode randomization, which randomized the mac address while scanning for new networks. For P, we are going to create a persistent mac address per SSID. So for enterprise use-case, you would see the device show up with the same mac address every time it connects to your network “

One direct implication: If the user forgets the network, and then reconnects a new MAC address is created for the SSID.  The same thing happens if the user factory resets their network settings.  Thus, operators will no longer be able to use the MAC as a reliable unique identifier for the device.

In this context, WBA community identified a list of potential impacts of these changes to existing systems and solutions:

- For MAC-based identification (e.g. MAC Authentication, MAC whitelisting, captive portal) MAC is cached on first time usage and subsequent logins re-use it. The customer would have to re-sign in and register the device each time the SSID is forgotten. This would result in a long list of devices per customers.

  - Also, this would  fill up the customers device limits.  The customer will subsequently find it difficult to identify their devices to specify which MAC addresses are the current ones that should be retained and which are invalid past identities that should be deleted.

- Android connection managers create profile on the fly, new MAC with every connection, will fail or will have to use WISPr for open

- Pay per use (PPU) customers have their pass associated with a MAC, if it changes there is no way to transfer that pass to another MAC. As noted that PPU use MAC Address authentication, this applies to Captive Portal ones as well

- Preemium customers can more easily get a new MAC that will allow them to create a duplicate account and get another free session / allowance, simply by forgetting the SSID.

- MAC randomization could result in duplication of a real registered MAC address, creating a spoofing scenario (theft of service, erroneous attribution)

- Analytics relies on ability to identify a unique device and have that identifier remain consistent over time

  - Helpdesks need to be able to identify specific devices that the customer is calling about, and understand how they have behaved over time.  If a user forgets the SSID because they are having connectivity problems, the service provider will lose traceability of the issue. It will also make it more difficult for the user to identify their device to the helpdesk advisor.

  - If a device has an association failure on first attempting to connect, will the same MAC address be used subsequently? If not, how can this failure be traced?

  - Access points / Service providers which track the history of devices that have connected will end up with bloated records which contain additional entries for devices where the user has forgotten the SSID and reconnected.

- Accounting and billing issues – MAC is tied to this in certain use cases.

- Blacklisting of devices – both for enterprise (BYOD) and home use.  For example, Not possible to use MAC address that has attached to the private network to block that MAC from connecting to public Wi-Fi in own home

- Passpoint considerations – Passpoint connection managers that create profiles on the fly may have the same behavior as a device who had forgotten the SSID.

  - For Passpoint connectivity, which is tied to service provider identity, not SSID, even maintaining the MAC address for a given SSID would be problematic as multiple SSIDs will typically be used for a single service provider. It would be better if the MAC address randomization maintained the MAC address for all connections to the specific service provider identity, not for connections to a specific SSID.

- Different bands with different SSID’s (2.4GHz and 5GHz) – Operators may see devices reported twice on their networks.  This also breaks band steering with multiple SSIDs.

- Client steering is affected if the probe requests use a different randomized MAC than used for association OR per probe.

- May impair the ability to enforce policies tied to specific devices, such as parental controls.  The user can forget the network and get a new MAC address, and network based parental controls would no longer be applied appropriately

In this context WBA would like to recommend further discussing with the operator community effective scenarios to minimize the impact of implementing such features and/or revising certain aspects that may help to resolve the concerns listed above.

For additional information and/or further questions please contact Bruno Tomas - WBA PMO (bruno@wballiance.com).

Next WBA F2F Meeting:

Possibly new bullets:

Need to take a clear stance – e.g.: we see a need for a unique identifier for customer experience.

Also this randomization needs to be reviewed against ITU article 19 to make sure implementations adhere to these requirements.

Also check how this relates to RLAN WRC-19.

iOS in probe only.  They discourage developers from using MAC address as a unique value.  Windows … ?

we need to clarify what each major OS is doing.  We should also gear the LS depending on the audience.  If we’re liaising to iOS we don’t want to confuse the issue by combining issues that don’t apply to the iOS implementation.  We can put non-iOS suggestions as a separate section.

What does this bullet mean? It’s not clear to me.

Why does analytics make the object of the “testing” group?

We propose removal of this item.

add specific use cases

generalize for whitelisting, blacklisting, etc – any per-device policy. Static IP assignment with MAC reservation.

This also goes with our greater discussion on policy.